## Slide 1: 2026.7.7 group meeting
Ultrasound probe scanning data collection system

## Slide 2: content
Step I: hospital side raw data collection
Step II: Lab side data converting
Step III: manual script writing
Step IV: future job

## Slide 3: Step I. System structure overview
Hospital side for raw data collection
Ultrasound scanning frame stream
Probe 6D homogeneous matrix tacked by AprilTag algorithm
Force data recorded by PAXINI finger tip sensor.
IMU for pitch and yaw angle recording

## Slide 4
Camera B
Camera A
AprilTag
Finger tip Sensor
IMU
Work Station
Rear perspective
Magnified probe perspective
Facility Setup for data collection Overview

## Slide 5: Step II: Lab side for data converting
data converting for Posture and Position
  Recording the tag pose change and real pose change from the encoders of the joints on manipulator
  AX = XB to calculate the transformation matrix X using the least square optimization

## Slide 6
data converting for force data converting
  Recording paxini finger tip force data and 6D force data.
  Using Universal Approximation Theorem to do the force mapping

## Slide 7: Step III: Manual script writing in progress…
…

## Slide 8: Paper content overview
Introduction and motivation (done)
Related work (literature review) (done)
System overview – data categories, data collection and calibration (done)
Demonstration interface design – the reasonability to collect some specific data and the process to collection (done)
Demonstration to robot data conversion interface – theorem applied to do the conversion (done)
Experiment
Future work and limitation

## Slide 9: Step Vi: future work, imitation learning
Strategy candidate: diffusion policy and ACT (action chunking with transformer)
Diffusion policy Advantages
Models multi-modal action distributions instead of averaging different demonstrations.
Generates smooth and coherent long-horizon trajectories.
Produces actions that are closer to expert demonstrations, leading to more natural robot motions.
More robust than conventional behavior cloning for complex manipulation tasks.
Limitations
Still relies on the training data distribution and has limited out-of-distribution (OOD) generalization.
Does not inherently understand task objectives; it only imitates demonstrated behaviors.
Requires a relatively large amount of demonstration data.
Iterative denoising increases inference latency compared with one-step action prediction.

## Slide 10
Acting chunking with transformer:
Advantages
Efficient one-step prediction with low inference latency.
Predicts action chunks for smooth and stable control.
Simple training with deterministic regression.
Well suited for tasks with consistent expert demonstrations.
Limitations
Learns a deterministic mapping and tends to average multi-modal demonstrations.
Limited ability to model action uncertainty.
Performance degrades when multiple valid future actions exist.
More sensitive to distribution shifts (OOD) than generative policies